## Slide 1
PROJECT REVIEW · 2026-08-26
vibe-pio
A cycle-accurate, formally verified model of the RP2350 PIO engine — and a solver that writes its programs.
iverilog · yosys · sby + z3 / boolector / yices · uv + ruff + ty + pytest
C0–C16 complete · 40 commits · 4 days
Notes: vibe-pio in one line: a formally verified PIO engine whose endgame is program synthesis. Built with open tools only, C0-C16 complete in four days.

## Slide 2
vibe-pio — project review · 2026-08-26
02 / 13
CONTEXT
PIO: programmable I/O on a dollar-class microcontroller
Nine instructions, four state machines. JMP · WAIT · IN · OUT · PUSH · PULL · MOV · IRQ · SET. Each SM is a tiny cycle-tight interpreter with its own shifters, FIFOs and fractional clock divider.
The “everything else” peripheral. Hard UART / SPI / I²C blocks cover the standards; PIO covers WS2812, Manchester, proprietary links — anything expressible as pin wiggles at cycle granularity.
Programs are hand-cycle-budgeted. .pio assembly where delay and side-set cycles are counted by hand against the datasheet. Correctness discipline is entirely on you.
PIO0
32×16 imem
4 SMs
PIO1
32×16 imem
4 SMs
PIO2
32×16 imem
4 SMs
48 GPIO pads
RP2350: 3 PIO blocks [SPEC-1-1] · one shared imem per block [SPEC-1-2] · 32-pin windows [SPEC-1-4]
That hand discipline is what this project attacks from both ends: verify the engine — then synthesize the programs.
Notes: PIO explainer for the room. End on the two-sided thesis: verification and synthesis.

## Slide 3
vibe-pio — project review · 2026-08-26
03 / 13
THE IDEA
Instruction memory is just state
Make instruction memory symbolic — a flat (* anyconst *) vector behind the SYM parameter. Assert the waveform you want on the pins, and let the SMT solver search the program space. The witness it returns is the program, by construction.
Behavioural spec
a C15 monitor over gpio_out:
“this must decode as a UART frame”
SymbiYosys run
SYM=1 frees all 32 words;
BMC / cover searches cycles × programs
Witness program
32 × 16-bit words, canonicalized
and disassembled back to .pio
Re-verified ×3
model replay · generated iverilog TB ·
bounded formal conformance
landed as C16 · make synth — cover/BMC only: free words make the state space the program space (SPEC-16-3)
The engine had to be formal-verification friendly for this to work — which is why vibe-pio exists.
Notes: The money slide. The swap point is confined to pio_instr_mem; surrounding RTL untouched. Cover/BMC only by design.

## Slide 4
vibe-pio — project review · 2026-08-26
04 / 13
DISCIPLINE
Spec-first, red/green, reproducible
Facts, not vibes — every load-bearing datasheet behaviour has a stable ID: 237 SPEC-x.y-n facts, 40 cycle-contract clauses (CC-n). RTL comments, assertions and tests cite them; the spec is never prose.
Red/green TDD — every bug a formal property uncovers gets a directed sim regression in the same commit — demonstrated red against the re-injected defect, then green. A check that has only ever passed may be vacuous.
Reproducible by container — iverilog, yosys, sby + z3 / boolector / yices pinned in one image; every gate is a make target; runtime scripts stay stdlib-only.
Kanban + grilling — planned work only on the board; loose ideas live in IDEAS.md and are promoted only after a grilling session; every commit records which agent did the work.
HOW A CITATION READS
// SPEC-3.4-11: autopull
// stall at cycle start
if (!rst) assert(...);
assert property (...)
##[...] $info("CC-7");
An assertion citing no fact is unsourced; a fact with no assertion is unverified. tools/trace_audit.py audits both directions (make audit).
Notes: The culture slide. Traceability is enforced by tooling, not convention.

## Slide 5
vibe-pio — project review · 2026-08-26
05 / 13
ARCHITECTURE
pio_block: one block, built and proven bottom-up
pio_instr_mem — 32×16, 1W / 4R async read (write visible to next fetch, CC-33)
u_sm0 : pio_sm
regs · decode · exec
shifters · FIFOs
u_sm1 : pio_sm
regs · decode · exec
shifters · FIFOs
u_sm2 : pio_sm
regs · decode · exec
shifters · FIFOs
u_sm3 : pio_sm
regs · decode · exec
shifters · FIFOs
instr[15:0] @ pc_r
reg bus
flat 9-bit map
CTRL … INSTR_MEM
one-clk retire
imem writes · per-SM config
W1C / force · TXF / RXF
pio_irq_flags 8 flags · PREV/NEXT/REL (CC-37)
pio_gpio_mux 2-FF sync · rotate · priority (CC-7)
pads
gpio_out / oe
irq_req / clr · flags
pin writes · in_bus
12 modules · 4,101 lines SV · built C1→C10, each with its own TB + sby proof before integration
monitors live in rtl/ — one tree for sim · formal · synth · pio_top (3 blocks + relay) designed, not yet built
Notes: Structure mirrors the hardware: shared imem, 4 named SM instances (no generate loop, for readable solver traces), registered flag paths for k-induction tractability.

## Slide 6
vibe-pio — project review · 2026-08-26
06 / 13
HISTORY
Four days, seventeen cards
PHASE 1 · BUILD THE ENGINE
PHASE 2 · BUILD THE SYNTHESIZER
08-23
13 commits
Spec consolidation — datasheet + pioasm cross-verified against pico-sdk and pico-examples; toolchain container; RTL conventions; C0 sim + formal infra.
08-24
12 commits
C1→C10 RTL, bottom-up: FIFOs, shifters, decoder, regs + divider, IRQ, GPIO mux, exec core, SM, block. Conformance: 20 pico-examples programs; UART loopback at fractional clkdiv.
08-25
11 commits
Python quality gate (uv · ruff · ty · pytest). C11 trace-equivalence miter; C12 golden model + assembler / disassembler. Hyperopt track grilled into KANBAN.
08-26
4 commits
C13 equivalence oracle; C14 hyperoptimizer (Pareto size × speed); C15 conformance monitors; C16 synthesis harness + witness pipeline.
source: git log @ 4f1eaef — 40 commits, 2026-08-23 → 2026-08-26
Notes: Two clean phases: verify the engine, then bolt the optimizer/synthesizer track on top. Kanban dependency order C11∥C12 → C13 → C14; C15 after C11; C16 after C12+C15.

## Slide 7
vibe-pio — project review · 2026-08-26
07 / 13
VERIFICATION
Every claim is a make target
make sim
directed iverilog testbenches per module + block + conformance — the fast gate every fix keeps green
make syn
yosys elaboration / hierarchy check per module
make formal
sby per module: BMC + k-induction (prove) + cover — assertions cite the SPEC-/CC- facts they verify
make model
Python golden model: cycle-accurate trace differential vs RTL; assembler bit-equal to pioasm
make equiv
program-pair equivalence oracle — model pre-filter, miter, sby verdict, replayed counterexamples
make hyperopt
rewrite search → Pareto front (imem words × ticks per loop); winners certified via equiv
make synth
symbolic imem cover → witness program, canonicalized and re-verified three independent ways
238
assertions, rtl + formal
13
sby task files
152
python tests + doctests
20
pico-examples programs
source: repo metrics @ 4f1eaef (grep / wc / ls)
Notes: The ladder from fast to deep. Nothing is 'believed' — everything is a command. 238 includes immediate assertions in RTL and formal properties.

## Slide 8
vibe-pio — project review · 2026-08-26
08 / 13
AGAINST THE REAL WORLD
Checked against silicon behaviour, not just self-consistency
Cross-checked against
The sources — spec assembled from the RP2350 datasheet and pioasm, cross-verified against pico-sdk and pico-examples; every fact pinned with a stable ID.
The examples — 20 official pico-examples PIO programs run unchanged on pio_block in sim.
The corners — UART loopback at the realistic fractional clkdiv (CF17); divider-invariance sweeps over the whole program matrix.
What the machinery caught
Manchester “tick divergence” — formal mismatch traced to a testbench wrap-constant defect; RTL exonerated after divider-invariance runs falsified the sync-margin theory first.
Golden-model transcription — differ caught: the FIFO-mode sampler must register the pre-edge mode; bus-decoded PUTGET index ≠ instruction aux index (SPEC-7-13 vs 3.7-4).
TB drive discipline — a posedge-driving TB variant silently dropped bus writes; negedge-drive is now the mandated idiom.
Formal findings get sim regressions — every bug above is re-checked red/green in the module testbench, in the fixing commit.
Notes: War stories build credibility. The manchester story: BMC counterexample -> hypothesis (sync margin) -> falsified by divider-invariance -> real cause was the TB's wrap constant.

## Slide 9
vibe-pio — project review · 2026-08-26
09 / 13
THE MOONSHOT TRACK
C11 → C16: from equivalence to synthesis
C11
Trace-equivalence miter
what “same behaviour” means: observable contract over pins + FIFOs, then a miter — SPEC-16
C12
Golden model + asm
cycle-accurate Python model; .pio assembler bit-equal to pioasm; disassembler — drives the search cheaply
C13
Equivalence oracle
make equiv: model pre-filter → miter → sby verdict; counterexamples decoded and replay-verified
C14
Hyperoptimizer
rewrite catalog searched to peephole closure; Pareto (imem words × ticks per loop); winners certified
C15
Conformance monitors
UART-TX frame + square-wave checkers over gpio_out — the spec-equality predicate
C16
Synthesis harness
SYM imem + monitor cover goals; witness canonicalized, disassembled, re-verified three ways
one source of truth: the model and the monitors are shared by sim, formal, hyperopt and synth — the referee is never a fork
Notes: Dependency order from the kanban grilling: C11 ∥ C12 → C13 → C14; C15 after C11; C16 after C12+C15.

## Slide 10
vibe-pio — project review · 2026-08-26
10 / 13
RESULT
Spec in, program out — then prove it again
Cover trace
sby returns a trace reaching the monitor’s done state, with imem free
Canonicalization
nop-fills and delay-preserving parks — one canonical program per witness
Disassembly
canonical words → .pio source via the C12 disassembler
Three-legged re-verify
C12 model replay + window check · generated iverilog TB · bounded formal conformance of the loaded witness
TARGET — SQUARE WAVE
half-period inside the CC-26 divider window
TARGET — UART-TX FRAME, ONE BYTE (8N1, 0xB2)
idle · start · 8 data bits LSB-first · stop — decoded by pio_mon_uart_tx (illustrative waveform)
red control
a deliberately contradictory spec returns UNSAT — proving the cover goals genuinely bind the solver, not just the seed program
Notes: C16 landed both targets: square-wave smoke and UART-TX-byte. Witness pipeline = SPEC-16-12; the UNSAT red case is committed.

## Slide 11
vibe-pio — project review · 2026-08-26
11 / 13
STATUS
Where it stands today
0
cards open on the kanban
C0–C16 done · board empty —
the next work is a choice, not a debt
per-module BMC + k-induction green (synth runs are cover/BMC by design)
conformance matrix green: 20 pico-examples programs + uart loopback
golden-model differential green; assembler bit-equal to pioasm
Known v1 limits — deliberate scoping, all on the record
Single-SM model scope — golden model + equivalence oracle run SM0 live (SPEC-16-4); multi-SM is the next model horizon.
Spec-only rewrites uncertified — side-set fusion and autopull overlay are catalogued and regression-cased, but the oracle’s spec-eq wiring is future work.
Interrupt composition partial — INTR exported; INTE/INTF/INTS stay stubs; NEXTPREV fan-out and GPIOBASE windowing belong to pio_top (designed, unbuilt).
Unpinned microsemantics — EXECCTRL.OUT_EN_SEL / INLINE_OUT_EN: docs carry one-liners only; blocked on silicon-level depth (IDEAS).
Sampling latency pinned in FV only — sim checks are shift-invariant by design; absolute input latency needs the formal CC-23 properties.
Notes: Honest scoping slide. Every limit is documented in DESIGN.md/IDEAS.md with the decision trail.

## Slide 12
vibe-pio — project review · 2026-08-26
12 / 13
DIRECTIONS
Where it could go next
FRONT-RUNNER · GRILLED ×2
TIS-100-style competitive PIO game, over SSH
Levels are receiver-style conformance monitors (the C15 machinery): a lenient UART sink decodes bytes and shrugs at framing errors — acceptance is “the receiver got the right data”, never golden-trace equality. The referee is tools/pio_model imported, never forked; the stored program is the object code itself. Hard gate before any of it: a legible live SM view — pc / x / y / isr / osr, FIFO levels, pin waveform strip, single-step. “If that cannot be made fun, the game dies there.”
Formal result cache — hash [script + files + toolchain] and reuse PASS verdicts; motivated by 20-minute z3 walls that dead-memory pruning later cut to seconds.
FPGA gate — iCE40 / ECP5 via yosys + nextpnr: a real-world synthesis check beyond the yosys elaboration pass.
Hardware-in-the-loop — property-based differential testing against actual RP2350 silicon via a capture rig (long-term).
Close the v1 gaps — multi-SM golden model, spec-eq wiring for the hyperoptimizer, pio_top 3-block assembly.
Notes: All from IDEAS.md. The game has survived two grilling rounds - it is the closest to promotion. C14's Pareto front is the natural scoring metric when it lands.

## Slide 13
vibe-pio — project review · 2026-08-26
13 / 13
vibe-pio — project review · 2026-08-26
Programs by construction.
The engine is proven against its spec. The optimizer’s rewrites are certified by an equivalence oracle. And now the synthesizer emits programs straight from behavioural specifications — every witness re-verified three independent ways.
make sim · make formal · make model · make equiv · make hyperopt · make synth
next on the board: your pick — the game, the cache, the FPGA gate, or closing the v1 gaps
Notes: Close on the arc: verify -> optimize -> synthesize. The ask: pick the next card.